## Slide 1: Introduction to Number System

## Slide 2: Common Number Systems
System | Base | Symbols
Decimal | 10 | 0, 1, … 9
Binary | 2 | 0, 1
Octal | 8 | 0, 1, … 7
Hexa decimal | 16 | 0, 1, … 9, A, B, … F
Notes: In any number system,
  Base = number of different digits (or combination of digits and letters) that a system of counting uses to represent numbers. E.g. base 10 means digits from 0 to 9
  Base is indicated by a subscript e.g. decimal number 974210

## Slide 3: Decimal Numbering System
How is a positive integer represented in decimal?
Let’s analyze the decimal number 375:
  375 = (3 x 100) + (7 x 10) + (5 x 1)
  = (3 x 102) + (7 x 101) + (5 x 100)
3
7
5
100
101
102
Position weights
Number digits
5 x100 = 5
7 x101 = 70
3 x 102 = 300
+
+
375
Notes: The value contributed by a digit equals the product of the digit times the weight of the position of the digit in the number
The weight of the rightmost (least significant bit LSB) is 100 (i.e.1)

## Slide 4: Why require other numbering systems?
Computers work only on two states: On/ OFF
  Basic memory elements hold only two states (either 0 or 1)
  Thus a number system with two elements {0,1} i.e. binary number system is used in digital world (1 binary digit = 1 bit.)
Binary numbers in text are a waste of space. Hex and Oct are really outstanding compressed representations of binary.
  Three bits make one octal digit
  E.g. 111 010 110 101 in binary can be represented as 7265 in octal
  Four bits make one hexadecimal digit
  E.g. 1110 1011 0101 in binary can be represented as EB5 in hex

## Slide 5: From Decimal to base n
Divide the decimal number repeatedly by the base, until you get a quotient less than base.
The answer can be written by writing all the remainders in reverse
Notes: Calculator: http://metricconversion.biz/57-octal-to-hexadecimal-conversion-numbers.html

## Slide 6: Decimal to Binary
Convert 2010 to base 2
2 20
10 0
5 0
2 1
1 0
Hence 2010 = 101002
Remainder
Notes: Trick for decimal to binary: https://www.youtube.com/watch?v=XdZqk8BXPwg

## Slide 7: Decimal to Octal
Convert 2010 to base 8
8 20
2 4
Hence 2010 = 248
Remainder

## Slide 8: Decimal to Hexadecimal
Convert 3010 to base 16
16 30
1 14
Hence 3010 = 1E16
Remainder
A=10
B=11
C=12
D=13
E=14
F=15

## Slide 9: From base n to Decimal
Multiply all digits with their positional weights (depending upon the base) and finally add them.

## Slide 10: Binary to Decimal
Convert 101002 to base 10
1 0 1 0 0
24 23 22 21 20
1*24 + 1*22 = 20
Hence 101002 = 2010

## Slide 11: Octal to Decimal
Convert 248 to base 10
2 4
81 80
2*81 + 4*80 = 20
Hence 248 = 2010

## Slide 12: Hexadecimal to Decimal
Convert 1E16 to base 10
1 E
161 160
1*161 + E*160
= 1*16 + 14*1 = 30
Hence 1E16 = 3010
A=10
B=11
C=12
D=13
E=14
F=15

## Slide 13: From Binary to base n
Three binary digits can be converted to one octal digit. Similarly, four binary digits can be converted to one Hexadecimal digit

## Slide 14: Binary to Octal Conversion
Three-bit Group Decimal Digit Octal Digit
000 0 0
001 1 1
010 2 2
011 3 3
100 4 4
101 5 5
110 6 6
111 7 7
Notes: No need to remember the positions, use positional weights method (421) to find out any number
For example 5 in octal is 101 in binary.

## Slide 15: Binary to Hex Conversion
Four-bit Group Decimal Digit Hexadecimal Digit
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 8
1001 9 9
1010 10 A
1011 11 B
1100 12 C
1101 13 D
1110 14 E
1111 15 F
Notes: No need to remember the positions, use positional weights method (8421) to find out any number
For example 9 in hexadecimal is 1001 in binary.

## Slide 16: Binary to Octal
Convert 101002 to base 8
Since 8 = 23, divide input in 3-bits groups, and convert to octal
Input = 1 0 1 0 0
Groups = 10 100
Pad with 0 010 100
Octal = 2 4
Hence 101002 = 248
Notes: pad empty digits with 0 for ease.

## Slide 17: Binary to Hexadecimal
Convert 101002 to base 16
Since 16 = 24, divide input in 4-bits groups, and convert to HEX
Input = 1 0 1 0 0
Groups = 1 0100
Pad with 0 0001 0100
Octal = 1 4
Hence 101002 = 1416

## Slide 18: From base n to Binary

## Slide 19: Octal to Binary
Convert 248 to base 2
Since 8 = 23, expand each single input to 3-bits binary
Input = 2 4
Conversion = 010 100
Hence 248 = 0101002 = 101002
Notes: Neglect initial zero

## Slide 20: Hexadecimal to Binary
Convert 1E16 to base 2
Since 16 = 24, expand each single input to 4 bits binary
Input = 1 E
Conversion= 0001 1110
Hence 1E16 = 000111102 = 111102

## Slide 21: Octal Hex conversions
No direct method.
For octal to hex conversion, convert Octal to binary and then to hex, and viceversa for hex to octal conversion.

## Slide 22: Octal to Hexadecimal
Convert 578 to base 16
  Convert octal to binary, then to hex
Input = 5 9
Binary Conversion= 101 111
4 bit groups 10 1111
Hex Conversion 2 F
Hence 578 = 2F16

## Slide 23: Hexadecimal to Octal
Convert 2F16 to base 8
Convert HEX to binary, then to octal
Input = 2 F
Binary Conversion= 10 1111
3 bit groups 101 111
Hex Conversion 5 7
Hence 2F16 = 578

## Slide 24: Practice Question
Convert given numbers to other number systems.
Decimal | Binary | Octal | Hexa- decimal
33 |  |  | 
 | 1110101 |  | 
 |  | 703 | 
 |  |  | 1AF

## Slide 25: Answer
Decimal | Binary | Octal | Hexa- decimal
33 | 100001 | 41 | 21
117 | 1110101 | 165 | 75
451 | 111000011 | 703 | 1C3
431 | 110101111 | 657 | 1AF